‘G1’ LOST WAX FISHPLATE

(REF:-  L13 = Brass or L14 Nickel Silver)

(NEW CRIMP UP TYPE)

Clean up any spru and straighten the cast parts as they may be slightly bent in the manufacture. Clean out the gap where the rails will go. To assemble:-The ‘round’ bolt head details goes on the inside of the rails, though it will not matter if they go the other way round.  Place under the rails and gently crimp together using blunt ended pliers, alternatively they can be crimped in a vice using a scrap piece of rail. When fitting allow for expansion of the rails, the linier expansion of brass rail is .00001 inch per degree Fahrenheit, this must be multiplied by the difference between maximum (150˚f) (surface temperature, not air temperature) and minimum (20˚f) temperature outdoors in the U.K. which is about 130 degrees, multiplied by 36” gives us a measurement of 47 thou per yard (or 1.2 mm).  So allow 1mm plus 1.2mm for 1 yard, 2.4mm for 2 yard and 3.6mm for 3 yard rail.  Now determine what temperature you are laying the track to give you your gap allowance.